## Slide 1: Introduction to Measurement Uncertainty
Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.
Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard." Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication. Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.
Date: 2006-3-02
Authors:

## Slide 2: Abstract
This presentation introduces the common industry concept of Measurement Uncertainty to represent the quality of a measurement.
Other common terms such as accuracy, precision, error, repeatability, and reliability are defined and their relationship to measurement uncertainty is shown.
Basic directions on calculating uncertainty and an example are included.
Notes: bet

## Slide 3: Overview
Definitions
Measurement Uncertainty
  Type A Evaluations
  Type B Evaluations
  Putting It All Together – RSS
  Reporting Uncertainty
  Special Cases
Example Uncertainty Budget
Summary
References

## Slide 4: Definitions
Error – The deviation of a measured result from the correct or accepted value of the quantity being measured.
There are two basic types of errors, random and systematic.

## Slide 5: Definitions
Random Errors – cause the measured result to deviate randomly from the correct value. The distribution of multiple measurements with only random error contributions will be centered around the correct value.
Some Examples
  Noise (random noise)
  Careless measurements
  Low resolution instruments
  Dropped digits

## Slide 6: Definitions
Systematic Errors – cause the measured result to deviate by a fixed amount in one direction from the correct value. The distribution of multiple measurements with systematic error contributions will be centered some fixed value away from the correct value.
Some Examples:
  Mis-calibrated instrument
  Unaccounted cable loss

## Slide 7: Definitions
Measurements typically contain some combination of random and systematic errors.
Precision is an indication of the level of random error.
Accuracy is an indication of the level of systematic error.
Accuracy and precision are typically qualitative terms.

## Slide 8: Definitions
Measurement Uncertainty combines these concepts into a single quantitative value representing the total expected deviation of a measurement from the actual value being measured.
  Includes a statistical confidence in the resulting uncertainty.
  Contains contributions from all components of the measurement system, requiring an understanding of the expected statistical distribution of these contributions.
  By definition, measurement uncertainty does not typically contain contributions due to the variability of the DUT.
    The “correct” value of a measurement is the value generated by the DUT at the time it is tested.
    Variability of the DUT cannot be pre-determined.
    Still, the uncertainty of a particular measurement result will include this variability.

## Slide 9: Definitions
Repeatability refers to the ability to perform the same measurement on the same DUT under the same test conditions and get the same result over time.
By repeating the test setup between measurements of a stable DUT, a statistical determination of System Repeatability can be made. This is simply the level of random error (precision) of the entire system, including the contribution of the test operator, setup, etc.

## Slide 10: Definitions
Reproducibility typically refers to the stability of the DUT and the ability to reproduce the same measurement result over time using a system with a high level of repeatability.
More generally, it refers to achieving the same measurement result under varied conditions.
  Different test equipment
  Different DUT
  Different Operator
  Different location/test lab

## Slide 11: Definitions
Reliability refers to producing the same result in statistical trials. This would typically refer to the stability of the DUT, and has connotations of operational reliability of the DUT.
Correction - value added algebraically to the uncorrected result of a measurement to compensate for systematic error.
Correction Factor - numerical factor by which the uncorrected result of a measurement is multiplied to compensate for systematic error.
Resolution – indicates numerical uncertainty of test equipment readout. Actual uncertainty may be larger.

## Slide 12: Measurement Uncertainty
A measurement uncertainty represents a statistical level encompassing the remaining unknown error in a measurement.
If the actual value of an error is known, then it is not part of the measurement uncertainty. Rather, it should be used to correct the measurement result.
The methods for determining a measurement uncertainty have been divided into two generic classes:
  Type A evaluation produces a statistically determined uncertainty based on a normal distribution.
  Type B evaluation represents uncertainties determined by any other means.

## Slide 13: Type A Evaluations
Uncertainties are determined through Type A evaluation by performing repeated measurements and determining the statistical distribution of the results.
This approach works primarily for random contributions.
  Repeated measurements with systematic deviations from a known correct value gives an error value that should be corrected for.
However, when evaluating the resulting measurement, the effect of many systematic uncertainties combine with random uncertainties in such a way that their effect can be determined statistically.
  Eg. A systematic offset in temperature can cause an increase in the random thermal noise in the measurement result.

## Slide 14: Type A Evaluations
Type A evaluation is based on the standard deviation of repeat measurements, which for n measurements with results qk and average value q, is approximated by:
The standard uncertainty contribution ui of a single measurement qk is given by:
If n measurements are averaged together, this becomes:
_

## Slide 15: Type B Evaluations
For cases where Type A evaluation is unavailable or impractical, and to cover contributions not included in the Type A analysis, a Type B analysis is used.
  Determine potential contributions to the total meas. uncertainty.
  Determine the uncertainty value for each contribution.
    Type A evaluation.
    Manufacturer’s datasheet.
    Estimate a limit value.
    Note: Contribution must be in terms of the variation in the measured quantity, not the influence quantity.
  For each contribution, choose expected statistical distribution and determine its standard uncertainty.
  Combine resulting uis and calculate the expanded uncertainty.

## Slide 16: Type B Evaluations
There are a number of common distributions for uncertainty contributions:
Normal distribution:
Examples:
  Results of Type A evaluations
  expanded uncertainties of components
where Ui is the expanded uncertainty of the contribution and k is the coverage factor (k = 2 for 95% confidence).

## Slide 17: Type B Evaluations
Rectangular distribution – measurement result has an equal probability of being anywhere within the range of –ai to ai.
Examples:
  Equipment manufacturer ± accuracy values (not from standard uncertainty budget)
  Equipment resolution limits.
  Any term where only maximal range or error is known.

## Slide 18: Type B Evaluations
U-shaped distribution – measurement result has a higher likelihood of being some value above or below the median than being at the median.
Examples:
  Mismatch (VSWR)
  Distribution of a sine wave
  5% Resistors (Culling)

## Slide 19: Type B Evaluations
Triangular distribution – non-normal distribution with linear fall-off from maximum to zero.
Examples:
  Alternate to rectangular or normal distribution when distribution is known to peak at center and has a known maximum expected value.

## Slide 20: Type B Evaluations
Another Look

## Slide 21: Putting It All Together - RSS
Once standard uncertainties have been determined for all components, including any Type A analysis, they are combined into a total standard uncertainty (the combined standard uncertainty, uc), for the resultant measurement quantity using the root sum of squares method:
where N is the number of standard uncertainty components in the Type B analysis.
The combined standard uncertainty is assumed to have a normal distribution.

## Slide 22: Reporting Uncertainty
The standard uncertainty is the common term used for calculations. It represents a ±1 span (~68%) of a normal distribution.
Typically, measurement uncertainties are expressed as an Expanded Uncertainty, U = k uc, where k is the coverage factor.
A coverage factor of k=2 is typically used, representing a 95% confidence that the measured value is within the specified measurement uncertainty.
Reporting of expanded uncertainties must include both the uncertainty value and either the coverage factor or confidence interval in order to assure proper use.

## Slide 23: Special Cases
For Type A analyses with only a small number of samples, the standard coverage factor is insufficient to ensure that the expanded uncertainty covers the expected confidence interval. Must use variable kp.
RSS math works for values in dB! However, distribution of a linear value may change when converted to dB.
  Uncertainties typically always determined in measurement output units.
N-1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 10 | 20 | 50 | 
kp | 14.0 | 4.53 | 3.31 | 2.87 | 2.65 | 2.52 | 2.43 | 2.37 | 2.28 | 2.13 | 2.05 | 2.00

## Slide 24: Special Cases
Not all distributions are symmetrical!
  Can develop asymmetrical uncertainties (+X/-Y) treating asymmetric inputs separately.
  Can separate random portion of uncertainty from systematic portion and apply a systematic error correction to measurement. (Convert asymmetric uncertainty to symmetric uncertainty.)
  error correction = (X+Y)/2, U = (X-Y)/2

## Slide 25: Example Uncertainty Budget

## Slide 26: Summary
This presentation gives common definitions for various terms that have been used and misused in the TGT draft.
The concept of measurement uncertainty has been introduced as the industry standard replacement for terms such as accuracy, precision, repeatability, etc.
Basic information has been given for a general knowledge of the concepts and components of measurement uncertainty.
This document is not intended as a reference! Please refer to the published documents referenced here.

## Slide 27: References
1. NIST Technical Note 1297-1994, “Guidelines for Evaluating and Expressing the Uncertainty of NIST Measurement Results”, Barry N. Taylor and Chris E. Kuyatt.
2. NIS-81, “The Treatment of Uncertainty in EMC Measurements”, NAMAS
3. ISO/IEC Guide 17025, “General requirements for the competence of testing and calibration laboratories.”