## Slide 1: Analyzing Atmospheric Convection from Variable Surfaces
Kylara Ruesch
Atms 360

## Slide 2: Arduino Board Setup
We build the Arduino’s to incorporate an IR sensor for surface temperature measurement, a Thermistor temperature sensor for atmospheric temperature measurement, a Chronodot for time measurement, a Digital pressure sensor (MS5637 GY37), and the Adafruit MicroSD card to save data.
I duct taped a 9v battery pack to the back for portable power.

## Slide 3: The IR Sensor
The IR Sensor had a 90 degree view field that allows it to absorb IR radiation from an object without needing direct contact.
It uses the I2C interface and connects with SDA and SCL pins (as well as ground and power), with which it gives a digital output of both the temperature of the object and the sensor casing itself.
Source: https://learn.adafruit.com/using-melexis-mlx90614-non-contact-sensors?view=all

## Slide 4: Measurement Setup
When taking measurements, I used a ruler to determine the height of the Thermistor from surface. I also used a wall/pillar for support on as many measurements as I could. This later turned out to introduce error in my IR data.
I plugged and unplugged the Arduino from the battery pack to turn it on and off for each measurement.

## Slide 5: Shaded Concrete
As can be seen in the IR graph (top left), the IR temperature of the concrete remained almost constant no matter the distance the sensor was away from it. This excludes the likely extraneous higher temperature for ground level as the spike may have come from accidental exposure of the sensor to my hand.
The thermistor measurement of atmosphere (bottom left) shows that temperature dropped at 1 inch from the ground. This may be indicative of a breeze or cold layer at that height. At higher altitudes, the temperature dropped step by step. This could be sue to the concrete retaining some heat from the previous day and passing it to the air by convection.

## Slide 6: Sunlit Concrete
The IR Graph for sunlit concrete (top right) shows that the temperature suddenly rose after ground level. This is likely due to an error on my part where I was next to a metal lined pillar (picture on bottom left). Metal reflects more IR radiation than concrete, so the increased view showed false higher temperature for the concrete. Please note that the ground temp for sunlit concrete is clearly higher than shaded concrete.
The Thermistor graph for sunlit concrete (bottom right) shows a lower temperature for ground than the IR sensor. This may be due to albedo, where the concrete may reflect more IR than it radiates, so it will appear to be hotter to the IR sensor while the thermistor takes a contact temperature and is unaffected by this problem.
The Thermistor graph also shows that air temperature rises then falls as the sensor increased in distance from the concrete. This could indicate convection of the heated concrete to air (as well as reflected sunlight energy) that heats up the air right above the concrete. The drop may be indicative of the inefficiency of air convection.

## Slide 7: Wet Grass
Unlike the previous surfaces, the IR Temperature for wet grass (top left) rose as the sensor was lifted higher. Perhaps this is due to evaporating water interfering with the IR reading of the grass the farther away the sensor got.
The atmospheric temperature (bottom left) also shows a rise in temperature with height. This could be due to rising heated air and water vapor from the grass in sunlight.
The two sensors appear to agree for temperatures all each level, so it is likely that the heated water vapor did interfere with the IR reading of the grass.

## Slide 8: Sunlit Asphalt
The IR temperature measurements (top right) showed near constant temperature for the asphalt, which hopefully means that there was less air interference with the reading.
The Thermistor reading (bottom right) indicate a drop in temperature right above the asphalt. This indicates that the asphalt retains more heat than it gives to the air for convection. A reading where we held the sensor above our heads (for Sky IR) indicted that temperature of air aright above the asphalt and multiple meters above it are nearly the same, reinforcing the poor convection idea.

## Slide 9: Sky
For a final measurement, we took the IR Temperature of the sky by holding the sensor above our heads (picture bottom left) and pointing it up. As seen in the graph (right), the sky is a much lower “surface” temperature than any of the surfaces we tested. This could be due to the cold nature of the lower levels of the atmosphere itself an also the far less intense IR radiation from areas other than the sun in the sky.

## Slide 10: Overview and Application
Asphalt appears to be the last convective to air surface followed by both concretes (shaded over sunlit). We grass appeared t have rising water vapor that interfered with IR readings.
For scientific applications, outdoor sensors for atmospheric and surface temperatures are best set far above an ground surfaces that aren’t wet or organic, away from reflective materials such as metal, and in a shaded spot.

## Slide 11: Questions?

## Slide 12: Thank you!