## Slide 1: Studying the Radiative Characteristics of Various Surfaces
Kelby todd |Atmospheric instrumentation

## Slide 2: Introduction
The purpose of this experiment was to study the surface and air temperatures of different surfaces and how the surface effects the surrounding air directly above.
The equipment used was the Arduino microcontroller in conjunction with the IR temperature sensor, thermistor, and the MS5637 GY37 digital pressure sensor as well as the Chronodot for time measurement.
The surfaces over which measurements were taken are as follows: concrete/shaded; concrete/direct sunlight; wet grass/direct sunlight; and asphalt/direct sunlight.
The measurements were taken from direct contact with the surface to 1 inch up to 5 inches above each surface.

## Slide 3: Arduino Microcontroller Setup

## Slide 4: Arduino Microcontroller Setup cont.
The Arduino microcontroller was setup for this experiment to be a mobile measurement device. It utilized an external battery carefully and scientifically duct taped to the Arduino.
The data was stored on a microSD card and transferred to Excel for analysis.

## Slide 5: Plot of Entire Data Set Over Every Surface
Chart: Time(24hr)

## Slide 6: Analysis of Entire Data set
As can be seen from the previous plot, the temperature fluctuates by about 20℃ over the period of the experiment.
There is a very odd downward spike from the IR sensor during the time that the sensor was pointed towards the clear sky. The large negative spike is probably due to the IR sensor registering air temperatures that had not yet been affected by heat convection from the asphalt surface.

## Slide 7: Measurement of Shaded Concrete
Chart: Time(24 hr)

## Slide 8: Analysis of Shaded Concrete Data
As can be seen in the plot over the shaded region of concrete, there is a cooldown time at the beginning due to the thermistor and IR sensor still being about as warm as it was inside of the physics building.
After the cooldown of the two devices, you can see that the temperature does not change much between each measurement in the shaded area.
Here it can also be seen that the straight lines signify the Arduino being off. And you can see the change in height between each measurement from those same straight lines.
There is an interesting spike in the thermistor measurement at about the point where the device was 4 inches off the surface. This may be due to me getting too close to the thermistor for a short period of time.

## Slide 9: Measurement of Sunlit Concrete
Chart: Time(24hr)

## Slide 10: Analysis of Sunlit Concrete Data
In this plot it can be seen that the temperature fluctuates a lot more in the thermistor measurements than in the IR measurements. The most interesting part of this is at about the 3 inch mark above the surface. The data shows that this was the coldest part of the measurement. This cold spot above the concrete may be the point where the warm ground has not yet heated up the air directly above it.
The temperature then rapidly rises again up to about 18.5℃ at the 4 inch mark above the concrete. I am unsure of why this happens here.
The IR temperature is at its lowest when the thermistor is in contact with the concrete but remains fairly steady as the height is increased, only rising a small amount between each measurement.

## Slide 11: Measurement of Wet Grass
Chart: Time(24hr)

## Slide 12: Analysis of Wet Grass Data
As can be seen in this plot, when the thermistor is in direct contact with the wet grass, the temperature fluctuates by about 7℃ whereas the IR sensor remains fairly constant around the 19℃ point. The fluctuations in the thermistor measurement are probably due to the sensor being wet and the fact that the grass had many small shaded and sunlit areas in the spot where measurements were taken.
Then the temperature steadily rises as the height is increased which is probably due to the convective properties of the wet grass.

## Slide 13: Measurement of Asphalt
Chart: Time(24hr)

## Slide 14: Analysis of Asphalt Data
As can be seen in the plot for the asphalt temperatures, the thermistor measurement is at its highest temperature of about 28℃ when the thermistor is in direct contact with the surface. This is pretty obvious because the asphalt is a darker surface and thus stores and radiates more heat when in direct contact with it.
After the peak temperature when the thermistor is no longer in direct contact with the surface, the temperature drops by nearly 11℃. This is probably due to the surface storing most of the heat energy transferred to it and not yet heating the air directly above it significantly.
Throughout this period of measurement, the IR temperature remains fairly steady and increasing slowly as the height is increased.

## Slide 15: Measurement Holding Arduino Towards the Sky
Chart: Time(24hr)

## Slide 16: Analysis of Measurements Pointing at the Sky
In this plot, it can be seen that the thermistor measurements do not change very much which is not surprising considering the convective heating of the air about 8 feet off the ground had not yet had a large effect.
The IR measurements are the interesting part. There is a large spike in temperature in an otherwise steady temperature reading. The spike in temperature may be due to having pointed the IR sensor at the moon in the daylight and the moon reflecting just enough infrared radiation for it to be noticeable in the data. Or it could be from momentarily pointing the sensor more in the direction of direct sunlight.

## Slide 17: Conclusion
To summarize, in this experiment we set out to determine how different surfaces affect the temperature of the air directly above each surface.
Each surface had different characteristics in how they affected the temperature at and directly above the surface. The darker surfaces obviously store more infrared radiation and therefore had a higher heat output upon measurement.
This lab easily illustrates how these different surfaces interact with the atmosphere directly surrounding them.
The Arduino microcontroller proved again to be a useful tool in easily being able to take many measurements over different regions over a fairly short period of time.