## Slide 1: Arduino unchained
By Paul Fremeau
Notes: For this experiment, we equip our Arduino with battery power and a micro-SD card interface, allowing us to untether from our computers and take measurements outside of the lab.

## Slide 2: Outdoor Arduino Temperature Study
For this study, the Arduino and integrated breadboard were outfitted with a thermistor, an infrared thermometer, a pressure sensor, a micro-SD card interface, and a Chronodot clock.
We left the confines of the lab, seeking knowledge of the relationship between ground surface temperature and ambient temperature as a function of height over various surface materials.
Notes: We began our day outside of the Leifson Physics Building, measuring the early morning temperature of the shaded concrete sidewalk in front of the building.

## Slide 3: The mlx90614
Infrared Thermometer
Works by detecting incoming infrared radiation and converting it to a temperature measurement of the object emitting the IR.
Sensor has a 90-degree field of view,
Measures object temperatures from -70 to +380 degrees Celsius.
Preferentially allows in thermal infrared radiation by using a silicon window.
Infrared radiation is absorbed by a black plate, which functions similarly to a digital camera sensor, measuring “brightness” of the infrared radiation.
Conversion from “brightness” to a temperature reading is performed on the chip, and the Arduino reads the output, converting to object temperature.
Notes: Here is a bit of information on the MLX90614 infrared thermometer that we used in this study, as well as some general theory on how temperature can be calculated from IR brightness.

## Slide 4
Sky Temp
Shaded Sidewalk Temp
Sunny Sidewalk Temp
Wet Grass Temp
Sunny Asphalt Temp
Notes: We began by measuring both surface IR temperature and ambient air temperature of a shaded concrete sidewalk, a sunlit concrete sidewalk, a sunlit wet grass lawn, a sunlit asphalt parking lot, and finally took the IR temperature of the blue sky.

## Slide 5
Chart: Thermistor Temperature vs Time over Variable Heights and Surfaces
Notes: The thermistor measured ambient air temperature at incrementally increasing heights above the ground. Height above ground was (very) generously approximated. For the shaded and sunlit concrete, and also for the asphalt, surface temperatures (measured by the thermistor) were greater than the ambient air temperatures at all heights measured. This makes sense, because the atmosphere warms from the ground up. The sun warms the surface, and the surface warms the air. There is a bit of a lag between surface temp and air temp as heating occurs over the span of a day.

## Slide 6
Chart: IR Temp vs Time for Variable Surfaces and Heights
Notes: It is interesting that the surface temperature of the shaded concrete sidewalk progressively cooled as the experiment commenced. It must have still been emitting more radiation than it was receiving, as it was still cooling down, and wasn’t in the sun quite yet. The other surface temperatures did not exhibit as robust of a trend. Perhaps their temperature trends would have been more evident had we spend more time measuring surface temperatures at each location.
We see that the sky has a low temperature, according to the IR thermometer. This also makes sense. The air is cold up there, and the air is the only source of infrared radiation, as long as a building, or maybe the sun, is not in the field of view of your sensor.

## Slide 7
Chart: Time (PDT)
Notes: Slopes are the similar for the temperature sensors. That helps to show that, even though my thermistor was measuring a lower temperature than the other two sensors, they were all probably measuring temperature, but might just need calibration.

## Slide 8: Time of Day
Time of day played a big role in this experiment. As we measured surface and ambient air temperature, insolation steadily increased as the sun moved higher in the sky. Hence, surfaces absorbed more and more solar radiation as the experiment commenced, and surface temperatures and ambient air temperatures rose as a direct effect of the increasing insolation.

## Slide 9
Here, the thermistor was held touching the ground for the duration of the measurement.