## Slide 1: Critical Review and Meta-analysis of ambient particulate matter source apportionment using receptor models in Europe C.A. Belis, F. Karagulian, B.R. Larsen, P.K. Hopke Atmospheric Environment 69 (2013) 94-108
Presented by
Jiaoyan Huang
@ATM 790
Univ. of Nevada, Reno

## Slide 2: Sections
Introduction
- air quality related models
Receptor modeling
- assumptions
- Incremental concentrations
- Enrichment ratio (ER/EF)
- Chemical mass balance (CMB)
- Principal component analysis (PCA)
- Factor analysis (FA)
Factor identification
Further discussions

## Slide 3: Introduction-air quality models
-Dispersion models: ISCST 3, AERMOD
-Gridded models: WRF-Chem, CMAQ, CAMx, GOES-Chem
-Receptor models: PCA, PMF
ALL MODELS ARE WRONG,
BUT SOME ARE USEFUL.

## Slide 4: Introduction-dispersion models
Advantages:
-relatively simple
Disadvantages:
-most of them do not have chemical reactions
-difficult to apply on the cases with multiple emission sources
-difficult to handle non-point sources
http://ops.fhwa.dot.gov/publications/viirpt/sec7.htm

## Slide 5: Introduction-gridded models
Advantages:
-most physical/chemical processes in the atmosphere are considered
-output with temporal/spatial variations
Disadvantages:
-need at least a small cluster computer
-emission uncertainties
-meteorological uncertainties
-not user friendly

## Slide 6: Introduction-receptor models
Advantages:
-simple and user friendly
-output with temporal variations
-can handle multiple emission sources
Disadvantages:
-assumptions are not always true
-results are varied with different locations
-most results are not quantitative
http://www.intechopen.com/books/air-quality/characteristics-and-application-of-receptor-models-to-the-atmospheric-aerosols-research

## Slide 7: Receptor modeling
Filter-based measurements, IMPROVE sites
Aerosol Mass Spectrum
Metals, trace elements
Organic, carbon species
Simple correlations, multiple linear regression
CMB,PCA, PMF, PSCF

## Slide 8: Receptor modeling
MAJOR ASSUMPTIONS
source profiles do not change significantly over time or do so in a reproducible manner so that the system is quasistationary.
receptor species do not react chemically or undergo phase partitioning during transport from source to receptor

## Slide 9: Receptor modeling Incremental concentrations approach
Lenschow et al., 2001 AE

## Slide 10: Receptor modeling Enrichment Factor
c could be from sea salt (Na, Cl) and soil (Al, Ca)
-Al and Si are the most common crust/reference spices
-EFs vary with locations
-many sources could be lumped together

## Slide 11: Receptor modeling Chemical Mass Balance
-emission profiles are needed
-multiple linear regression
-weighting factors with uncertainties

## Slide 12: Receptor modeling Principal Component Analysis
To convert a set of observations of possibly correlated variables into a set of values of linearly uncorrelated variables
Hopke, personal communication

## Slide 13: Receptor modeling Positive Matrix Factorization
A weighted factorization problem with non-negativity constraints using known experimental uncertainties as input data thereby allowing individual treatment (scaling) of matrix elements

## Slide 14: Receptor modeling PCA vs FA(PMF)
PCA aims to maximize the variance by minimizing the sum of squares
FA relies on a definite model including common factors, specific factors and measurement errors
PCA has a unique solution
In PCA, variables are almost independent from each other while common factors (communalities) contribute to at least two variables
FA is considered more efficient than PCA in finding the underlying structure of data
PCA and FA produce similar results when there are many variables and their specific variances are small

## Slide 15: Sources identification Organic compounds
Zhang et al., 2011 ABC
POA from fossil fuel-hydrocarbon organic aerosol
Cooking related OA-hydrocarbon organic aerosol with diurnal pattern
Biomass burning-m/z 60-73, levogluvosan
LV-OOA
SV-OOA

## Slide 16: Sources identification
Sea/Road salt: Na, Cl, and Mg
Crustal dust: Al, Si, Ca, and Fe
Secondary inorganic aerosol: S, NO3
Oil combustion: V, Ni, S
Coal combustion: Se, PAHs
Mobile sources: Cu, Zn, Sb, Sn, EC, Pb
Metallurgic sources: Cu, Fe, Mn, Zn
Biomass burning: K, levoglucosan

## Slide 17: Sources identification
H. Guo et al. / Atmospheric Environment 43 (2009) 1159–1169
Receptor modeling of source apportionment of Hong Kong aerosols and the implication of urban and regional contribution

## Slide 18: Sources identification
H. Guo et al. / Atmospheric Environment 43 (2009) 1159–1169
Receptor modeling of source apportionment of Hong Kong aerosols and the implication of urban and regional contribution

## Slide 19: Future discussions
Y. Wang et al. / Chemosphere 92 (2013) 360–367

## Slide 20: Future discussions PSCF
Sampling site
Cell 1
Cell 2
Back-trajectory representing high concentration
Back-trajectory representing low concentration
PSCF value
Cell 1 = 2/3
Cell 2 = 0/2
Notes: The algorithm of PSCF is to count each trajectory endpoint that terminates within the grid cell.
The trajectory that contains high Hg concentration is counted to increase the probability.

## Slide 21: Future discussions
I. Hwang, P.K. Hopke / Atmospheric Environment 41 (2007) 506–518

## Slide 22: Future discussions
I. Hwang, P.K. Hopke / Atmospheric Environment 41 (2007) 506–518

## Slide 23: Future discussions 3D- PMF
N. Li et al. / Chemometrics and Intelligent Laboratory Systems 129 (2013) 15–20

## Slide 24: Future discussions 3D- PMF
N. Li et al. / Chemometrics and Intelligent Laboratory Systems 129 (2013) 15–20

## Slide 25: Supporting information
Prof Hopke @ Clarkson Uni.
http://people.clarkson.edu/~phopke/
EPA PMF 3.0
http://www.epa.gov/heasd/research/pmf.html
EPA PMF 4.1 Prof Larson @ UW
http://faculty.washington.edu/tlarson/CEE557/PMF%204.1/
The most current version PMF 5.0 US EPA is still working on it.

## Slide 26: Questions??