## Slide 1
Remote sensing of particulate pollution from space: Have we reached the promised land?
by
Hoff and Christopher, 2009

## Slide 2
Outline
Aerosol Definitions
Purpose of the paper
Background
Satellite observations for air quality purposes
Type of satellites
Remote sensing from space
PM2.5/AOD relationships
Fundamental problems
Summary

## Slide 3
Outline
Aerosol Definitions
Purpose of the paper
Background
Satellite observations for air quality purposes
Type of satellites
Remote sensing from space
PM2.5/AOD relationships
Fundamental problems
Summary

## Slide 4
Aerosol
It is a suspension of fine solid particles or liquid droplets in a gas.
Anthropogenic: Causes by human activities
Natural: Causes by the nature

## Slide 5
Why do people study aerosols?
Climate effects
Climate effects
Impact in the radiative forcing
Cooling the atmosphere
Warming the atmosphere
Light absorption
Light scattering
Human health

## Slide 6
Outline
Aerosol Definitions
Purpose of the paper
Background
Satellite observations for air quality purposes
Type of satellites
Remote sensing from space
PM2.5/AOD relationships
Fundamental problems
Summary

## Slide 7
50th anniversary
Since the first satellite observation
1995-2009
Development of 42 instruments relevant for air quality.
Importance:
Event detection
Purpose
Trace gases and aerosols
Transport and model prediction
Emission estimation
Satellite observations

## Slide 8
Outline
Aerosol Definitions
Purpose of the paper
Background
Satellite observations for air quality purposes
Type of satellites
Remote sensing from space
PM2.5/AOD relationships
Fundamental problems
Summary

## Slide 9
Background: Explorer 7 (1959)
Explorer Vll
Suomi
IR radiative heat balance as a forcing agent for atmospheric circulation
Explorer 7 | 
Mission type | Earth science
Operator | NASA
Mission duration | 2 years

## Slide 10
Background: TIROS
TIROS I (or TIROS-1) was the first successful low-Earth orbital weather satellite, and the first of a series of Television Infrared Observation Satellites. It was launched by NASA and partners on April 1st, 1960
First image of the Earth
Features such as
Satellite technology was developed
1961
Clouds
Weather systems
Tool to identify present and future weather

## Slide 11
This critical review discusses the measurement of air quality- related gases and aerosols from monitors orbiting above the atmosphere.
Main purpose:
The National Academy of Sciences
(NAS)
Expectation
Routine monitoring
Tropospheric pollution
Public health
Constrains:
Orbit
Atmospheric transparency
Wavelength of observation
Scattering and absorption
Molecular spectroscopy
Scattering

## Slide 12
Outline
Aerosol Definitions
Purpose of the paper
Background
Satellite observations for air quality purposes
Type of satellites
Remote sensing from space
PM2.5/AOD relationships
Fundamental problems
Summary

## Slide 13
Satellite observations for air quality monitoring
Several reviews examine observations of trace gas species and aerosols from space.
“…Geostationary satellite observations
of chemically reactive trace gases will provide unique insight into the evolution and extent of air pollution with the temporal resolution necessary to address air quality on a daily basis…”
NRC report:
Near-real-time forecasting of O3 and PM
Identification of transport events
Air quality information needed
Source identification
Long-term composition
Regulatory compliances
Management of haze
Class l areas
Exposure
Heath impact

## Slide 14
Satellite observations for air quality monitoring
Several reviews examine observations of trace gas species and aerosols from space.
“…Geostationary satellite observations
of chemically reactive trace gases will provide unique insight into the evolution and extent of air pollution with the temporal resolution necessary to address air quality on a daily basis…”
NRC report:
Near-real-time forecasting of O3 and PM
Identification of transport events
Air quality information needed
Source identification
Long-term composition
Regulatory compliances
Management of haze
Class l areas
Exposure
Heath impact
Air quality compliance, atmospheric composition and trends, alerts, near-real-time forecasting, and determination of visibility impairment are addressed in some fashion by satellite measurements.

## Slide 15
Outline
Aerosol Definitions
Purpose of the paper
Background
Satellite observations for air quality purposes
Type of satellites
Remote sensing from space
PM2.5/AOD relationships
Fundamental problems
Summary

## Slide 16
Satellites orbits:
Hoff et al. 2009
Satellites orbits
Spatial and temporal resolution
< 2,000 km
35,785 km
2,000-25,000 km
Low
(LEO)
Medium
(MEO)
Geosynchronous
(GEO)

## Slide 17
Satellite Remote sensing
Satellite Sensors
Passive: measure energy that is naturally available
Active: The sensor emits radiation which is directed toward the target. The radiation reflected from that target is detected and measured by the sensor
Types of Orbits
Geostationary: Appears ‘fixed’ above earth
Polar: synchronous orbit with orbital pass at about same local solar time each day

## Slide 18
Geostationary satellites :
Geo
Orbit: once a day
Equatorial position
Penalty
Large and complicated
Heavy and expensive to launch
High spatial and temporal resolution

## Slide 19
Low orbit satellites :
Leo
Orbit: ~1.5 hr
Altitude:
250 to 500 km
Satellite crosses the Earth-
Sun vector
Same local time each day
Ascending or descending node is fixed

## Slide 20
Satellite Remote sensing
NASA A-Train
A-Train
A-Train (Afternoon train)
Satellite constellation
Sun-synchronous orbit
Orbit Inclination: 98.140
Cross the Equator at 1:30 p.m.
Purpose
High definition, 3-D images of the Earth’s atmosphere and surface
A-Train
Active
AQUA
CloudSat
CALIPSO
Aura
Past and Failed
PARASOL
OCO
Glory
GCOM-W1

## Slide 21
Satellite Remote sensing
Aqua May-4-2002
Ascending orbit satellite
Moves from South to North
Afternoon satellite
Overpass at 1:30 p.m. local time
Altitude
705 km
Inclination
980
Period
99 min.
16 orbits per day
Instruments
AMSR-E
MODIS
AMSU-A
AIRS
HSB
CERES

## Slide 22
Satellite Remote sensing
Terra Dec-18-1999
Descending orbit satellite
Moves from North to South
Morning satellite
Overpass at 10:30 a.m. local time
Instruments
ASTER
CERES
MISR
MODIS
MOPITT
Altitude
705 km
Inclination
98.50
Period
99 min.
16 orbits per day

## Slide 23
Outline
Aerosol Definitions
Purpose of the paper
Background
Satellite observations for air quality purposes
Type of satellites
Remote sensing from space
PM2.5/AOD relationships
Fundamental problems
Summary

## Slide 24
Remote sensing: From Orbit
Collecting information about an object without being in direct physical contact with it.
LIMITATION: Cloud cover and bright surfaces significantly limit satellite observations of air quality.
Observation are made:
Wavelengths
From 260 nm in the ultraviolet (UV)
To radar wavelengths (0.1–10 cm).
Atmospheric transparency is needed
Probe down to the surface.

## Slide 25
Aerosol
Definitions
Aerosol Optical Depth (AOD): is the degree to which aerosols prevent the transmission of light by absorption or scattering of light
-slope=TOD
Beer’s law
α : Extinction coefficient of the atmosphere
λ: Wavelength
z: physical path
Io: source radiance
I :radiance passing to the satellite
If the path is vertical, z is the altitude of the source.
++
+
Hoff et al. 2009

## Slide 26
Passive remote sensing in the IR spectrum: Some applications
1. Surfaces temperature because in IR the atmosphere is transparent.
Ocean e~0.98
Land: e~0.7 to 0.98
2. Fires detection
Loria et al. 2013
Loria et al. 2013

## Slide 27
Passive remote sensing in the visible spectrum
In the UV (250– 400 nm) and visible (400–700 nm) range of wavelengths, the Sun’s input and reflected light dominate the radiance being emitted back to space.
Visible
Aerosol dominates
Light scattering
Strongly dependent on the visible spectrum
Particle size and wavelength are equal
Mie extinction efficiency peaks
2-D solution:
I: radiance
Tau: is zero at TOA and is a variable of the
downward path
µ=cosθ(negative downwards)
ω: single-scatter albedo
p(Ω,’ Ω):scattering
phase
3D solutions are required in the
presence of clouds

## Slide 28
Uplooking instruments
The AOD of the atmosphere is monitored globally using the Sun as a source and measuring the transmittance as a function of solar elevation angle (or equivalently the knowledge of the air mass). The calibration of a sunphotometer is done via the Langley regression
AErosol RObotic NEtwork [AERONET]
Photometrie pour le Traitement Operationnel
de Normalization Satellitaire [PHOTONS]
SKYNET
Multifilter Rotating Shadowband and Radiometer [MSRFR]
World Meteorological Organization Global Atmosphere Watch Physikalisch-Meteorologisches Observatorium Davos [WMO/GAW/PMOD]
These networks serve as “truth” for satellite remote sensing because the instruments are stable, well-calibrated, well-characterized, and can use sophisticated techniques to quality assure that clouds and anoise are minimized. For space-borne remote sensing of AOD, most satellite instruments have been tested against sunphotometer results.

## Slide 29
Inversion of Sun and Sky Radiance to Derive Aerosol Properties from AERONET. (Holben et al., 2003)
Uplooking instruments
Notes: Aerosol volume and size distribution are retrievable by inversion modelling from the spectral aerosol optical depth.

## Slide 30
http://www.ge.infn.it/iba/ambiente_en.html
Through satellite retrievals is possible quantify Particulate Matter (PM):
PM10
PM2.5
PM1
Light scattering
Roughly proportional to cross-sectional area
Volume
Proportional to the cube of the radius
Relationship between scattering and mass
Approximately linearly related to particle size
If particle size is constrained to submicrometer modes
Light scattering is most important
Illumination is highest
Strong correlations between scattering and mass

## Slide 31
Satellite Remote sensing
MODIS: Moderate-resolution Imaging Spectroradiometer
MODIS
Aqua and Terra
AOD over ocean
AOD over land
7 wavelengths (470-2130 nm)
3 wavelengths (470, 660, and 2130 nm)
Goal of 5% relative uncertainty
Goal of 15% relative uncertainty
Dark-Target algorithm
Deep- blue algorithm
Dark vegetated surfaces
Bright surfaces (Deserts)
Dark-Target algorithm
Dark ocean surfaces

## Slide 32
Active remote sensing from space and the ground (Lidar)
Lidar measures:
Backscatter coefficient of the aerosol
In principle lidar can be used
Infer the vertical profile of extinction
Then integrate to obtain the optical depth
HOWEVER!!!!!!!!!!!!!!!
Returned signal is not only proportional to the backscatter coefficient of the aerosol
In principle, lidar profiles may be as useful (or more useful) than a column measurement because one could examine the extinction closest to the surface rather than integrated over the observation path.

## Slide 33
Outline
Aerosol Definitions
Purpose of the paper
Background
Satellite observations for air quality purposes
Type of satellites
Remote sensing from space
PM2.5/AOD relationships
Fundamental problems
Summary

## Slide 34
Use of AOD to assess ground-based concentrations: PM2.5/AOD relationships
Assumptions
Cloud-free skies
Well-mixed boundary layer
All the aerosol are within the boundary layer
Similar optical and chemical properties from day to day
f(RH): ratio of ambient and dry extinction coefficients
ρ: aerosol mass density
Qext-,dry : Mie extinction efficiency
reff: particle effective radius
S: specific extinction efficiency of the aerosol at ambient relative humidity
H: Boundary layer height
Most papers have addressed PM2.5/AOD and a few PM10/AOD.

## Slide 35
Use of AOD to assess ground-based concentrations: PM2.5/AOD relationships
Hoff et al. 2009

## Slide 36
Use of AOD to assess ground-based concentrations: PM2.5/AOD relationships
2004-2006 studies
Best correlations in the U.S. northeast (R> 0.8)
Aerosol type
Poorest in the U.S. northwest (R~0.2)
Wider variation in aerosol types
Mixing height
More smoke than the east
Higher surface reflectivities
More nitrate than sulfate
More elevated plumes
The most uniform in:

## Slide 37
Use of AOD to assess ground-based concentrations: PM2.5/AOD relationships
Simple linear relationships between AOD and PM2.5 were applicable only for certain seasons and locations
Model improvement
PM2.5 estimations from satellite AOD
Combination
MISR
Weather variables
Planetary boundary layer height
346 EPA daily averaged ground monitors
RH from the GEOS-3
Results have shown:
As the PBL increased, the PM decreased by roughly the cube root of PBL.
It also would predict that P/A would be largest for small AOD and flatter for large AOD.
Studies done out of the U.S. showed that the correlation coefficients averaged over all locations was R~ 0.96

## Slide 38
Use of AOD to assess ground-based concentrations: PM2.5/AOD relationships
The assumption in this equation that one has a well-mixed boundary layer does not often hold. Factors that lead to differing correlations in this equation are types of aerosol, surface type, whether overlying aerosols have been removed from the regression, whether the aerosol is really on the surface, definitions of PM2.5, and satellite precision in determining AOD
Some solutions:
Use of lidar
Determine cases of elevated aerosol
Use of AOD/H
New regression variables in the model
Show an improvement from R~0.36 to R~0.75 in San Joaquin Valley CA
Problems with the accuracy of the current PBL prediction. It s required the use of lidar PBL
heights, when available, as a validation for the model

## Slide 39
Use of AOD to assess ground-based concentrations: PM2.5/AOD relationships
Linear model
Neural network model
relationship using eight expected dependencies
on two input variables (PM2.5 and AOD)
In the Southeast U.S.
Multi-linear model
New variables: PBL height, location,
temp, RH
In the Southeast U.S.

## Slide 40
Events, atmospheric process research, and trends

## Slide 41
Outline
Aerosol Definitions
Purpose of the paper
Background
Satellite observations for air quality purposes
Type of satellites
Remote sensing from space
PM2.5/AOD relationships
Fundamental problems
Summary

## Slide 42
Some fundamental problems in satellite remote sensing
Trace gases: the conversion of mixing ratio to extinction requires the knowledge of the absorption coefficient of the gas at a given pressure and temperature.
The visible absorption measurements for O3, SO2, and NO2 are relatively wide spectral measurements, the absorption coefficient is reasonably well known and easy to characterize.
For these gases, the column measurement from passive instruments may be sufficient to characterize a mass budget.
Aerosol
Extensive properties
Microphysical property of the pollutant is not constant
Composition
Size
Indices of refraction
Hydration

## Slide 43
Some fundamental problems in satellite remote sensing
Clouds
Clouds cover 60–70% of the planet at any
time
Clouds obscure the surface and make detection of aerosols at the surface impossible
This limitation is significant during winter months
At midlatitudes
The rainy seasons in the tropics.

## Slide 44
Some fundamental problems in satellite remote sensing
Snow
The high surface reflectivity of snow is problematic at wavelengths that rely on dark surfaces for detection of extinction contrast

## Slide 45
Some fundamental problems in satellite remote sensing
Bright surfaces
Like deserts or bare soil
Do not provide enough contrast with the added radiance from aerosols to be able to retrieve AOD
Deep blue algorithm
Hsu and her colleagues used the shortest wavelength from MODIS to push the contrast between the surface reflectance and aerosol reflectance beyond the traditional MODIS AOD retrieval.

## Slide 46
Outline
Aerosol Definitions
Purpose of the paper
Background
Satellite observations for air quality purposes
Type of satellites
Remote sensing from space
PM2.5/AOD relationships
Fundamental problems
Summary

## Slide 47
Satellite air quality measurements are in their infancy with 50 yr of history of atmospheric composition measurements but less than 10 yr of record with modern multisensor platforms from polar and geostationary orbits.
Success has been shown at retrieving the column of several gases in visible and IR wavelengths.
Aerosols have been quantified using the AOD and the relationship between AOD and PM2.5 is being actively investigated.
Summary

## Slide 48
Satellite air quality measurements are in their infancy with 50 yr of history of atmospheric composition measurements but less than 10 yr of record with modern multisensor platforms from polar and geostationary orbits.
Success has been shown at retrieving the column of several gases in visible and IR wavelengths.
Aerosols have been quantified using the AOD and the relationship between AOD and PM2.5 is being actively investigated.
Summary

## Slide 49
Satellite air quality measurements are in their infancy with 50 yr of history of atmospheric composition measurements but less than 10 yr of record with modern multisensor platforms from polar and geostationary orbits.
Success has been shown at retrieving the column of several gases in visible and IR wavelengths.
Aerosols have been quantified using the AOD and the relationship between AOD and PM2.5 is being actively investigated.
Summary

## Slide 50
Although the desire for the use of satellite data for air quality purposes is widely stated, the reality is that many of the measurements have not yet met the promise that they can be operationally used for today’s air quality monitoring requirements.
Combining multiple measurements and models improves the understanding of the physics of the measurement and improves the precision.
Strengths of satellite measurement are found in emissions identification (fires especially), event tracking and transport, definition of boundaries of large-scale pollution features, and providing some evidence for profiles of pollutants well above the surface.
Summary

## Slide 51
Although the desire for the use of satellite data for air quality purposes is widely stated, the reality is that many of the measurements have not yet met the promise that they can be operationally used for today’s air quality monitoring requirements.
Combining multiple measurements and models improves the understanding of the physics of the measurement and improves the precision.
Strengths of satellite measurement are found in emissions identification (fires especially), event tracking and transport, definition of boundaries of large-scale pollution features, and providing some evidence for profiles of pollutants well above the surface.
Summary

## Slide 52
Although the desire for the use of satellite data for air quality purposes is widely stated, the reality is that many of the measurements have not yet met the promise that they can be operationally used for today’s air quality monitoring requirements.
Combining multiple measurements and models improves the understanding of the physics of the measurement and improves the precision.
Strengths of satellite measurement are found in emissions identification (fires especially), event tracking and transport, definition of boundaries of large-scale pollution features, and providing some evidence for profiles of pollutants well above the surface.
Summary

## Slide 53
Passive remote sensing in the visible spectrum
In the UV (250– 400 nm) and visible (400–700 nm) range of wavelengths, the Sun’s input and reflected light dominate the radiance being emitted back to space.
Gases with absorption features
O3
Sulfur dioxide [SO2]
NO2
Formaldehyde
[HCHO]
Glyoxal [CHOCHO]
Visible
Aerosol dominates
Light scattering
Strongly dependent on the visible spectrum
Particle size and wavelength are similar
Mie extinction efficiency peaks

## Slide 54
Passive remote sensing in the IR spectrum
Source radiance from the surface
Source radiance from the top of the atmosphere
Thermal emission from the atmosphere

## Slide 55
Uplooking instruments
-slope=TOD

## Slide 56
AERONET: Inversion assumptions 2012…
Atmosphere is assumed plane-parallel.
Aerosol particles are assumed to be partitioned into two components: spherical and non-spherical.
The spherical component is modeled by an ensemble of polydisperse, homogeneous spheres (complex index of refraction is the same for particles of all sizes).
The non-spherical component is a mixture of polydisperse, randomly-oriented homogeneous spheroids
Vertical distribution of aerosol is assumed homogeneous in the almucantar inversion and bi-layered for the principal plane inversion.

## Slide 57
Occultation and near-nadir viewing
Measurements of trace gases from space in the UV
Require:
High concentration
Present above approximately 2 km
Example: Volcanic plume detections

## Slide 58
Satellites orbits:
Satellite position:
Semi-major axis of the orbit
The eccentricity
Longitude of the ascending node
Periapsis
Mean anomaly
a
c
eccentricity=c/a

## Slide 59
CALIPSO (Cloud-Aerosol Lidar and Infrared Pathfinder Satellite
Observation APR-28-2006
Instruments
CALIOP
WFC
IIR
Ascending orbit satellite
Moves from South to North
Afternoon satellite
Overpass at 1:30 p.m. local time
Cloud-Aerosol Lidar with Orthogonal Polarization
Altitude
705 km
Inclination
980
Period
99 min.
16 orbits per day