## Slide 1: Unmanned Aircraft Systems Applications in Science
Presented by Jayne Boehmler
April 24, 2017

## Slide 2: Background Paper
    Unmanned Aircraft Systems in Remote Sensing and Scientific Research: Classification and Considerations of Use
    Adam C. Watts 1*, Vincent G. Ambrosia 2 and Everett A. Hinkley
    8 June 2012

## Slide 3: What is UAS?
Federal Aviation Administration (FAA) definition:
    “An unmanned aircraft system (UAS), sometimes called a drone, is an aircraft without a human pilot onboard – instead, the UAS is controlled from an operator on the ground.”

## Slide 4: History of UAS
The use of unmanned flight pre-dates human-piloted flight
Unmanned hot-air balloons used in aerial bombardment of Venice in 1849 and the American Civil War (1861-1865)
Corporal William Eddy of the US Army used remotely-triggered cameras aboard kites in the 1898 Spanish-American War
The Cold War spurred interest among the scientific community in utilizing UAS for science missions
“three Ds” dull, dirty, or dangerous missions

## Slide 5: History of UAS
NASA developed unmanned aircraft for high-altitude atmospheric sampling during the “Mini-Sniffer” program of the 1970s–1980s
NASA’s Environmental Research Aircraft and Sensor Technology (ERAST) program in the 1990s marked the first major steps towards developing the protocols and capabilities for employment of UAS supporting scientific research.

## Slide 6: UAS Scientific Applications
Mapping of Natural Resources
    Vegetation growth, decline, and species invasion
Power Infrastructure Inspection
    Inspection of wind turbine blades for signs of deterioration and power line survey
Remote Sensing
Agricultural Operations
Fire Monitoring
Search and Rescue
Aerial Mapping and Meteorology
    Cloud Seeding
    Snow Pack
    Topography
Sports event film coverage
Fisheries protection
Disaster Analysis

## Slide 7: Objectives of the paper
To describe various classes and categories of UAS and considerations for their use.
(2) To describe the general types and capabilities of sensor packages available for UAS, and their relative suitability for representative scientific applications.
(3) To introduce important principles of government regulation of UAS, with specific examples from the USA and Europe.

## Slide 8: Categories
High Altitude, Long Endurance (HALE)
  larger than many general-aviation manned aircraft
  Altitudes 20,000 m +
  30+ hours thousands of km
Medium Altitude, Long Endurance (MALE)
  Altitudes up to 9,000 m
  Flight range hundreds of km
  Flight time lasting several hours
Low Altitude, Long Endurance (LALE)
  Payload capabilities of several kg
  Altitudes of a few thousand meters
Low Altitude, Short Endurance (LASE)
  Wing span <3 m
  Launched by hand
Vertical Take-Off & Landing (VTOL)
  Capable of hovering
Micro (or miniature) Air Vehicles (MAV)
  Altitudes <330 m, 5-30 min flights
Figure 1. Image courtesy of US Department of Homeland Security [7].

## Slide 9: Micro (or miniature) Air Vehicles (MAV)
The AV Nano Hummingbird is the size of a small bird (weight of 19 g and wingspan of 16 cm) and can climb and descend vertically, fly in all horizontal directions, is equipped with a small video camera, and has a flight endurance of ~8 min
Very small UAS or Micro-UAVs (MAVs) and Nano UAVs (NAVs)
Began in the mid-late 1990s supported by the US Department of Defense.
Designed for short mission profile surveillance platforms
Allows observation capabilities in confined spaces or hostile environments in military applications
Figure 2. Courtesy AeroVironment, Inc. (http://www.avinc.com)
Notes: gather information for law enforcement and may have some utility for wildlife inventories and other remote sensing civilian applications

## Slide 10: Vertical Take-Off & Landing (VTOL)
Most VTOL UAV history dates to the early 1960s
Major developments occurred in the 1990s and the present.
Portable
Platforms for remote areas
Limited sensor payload capabilities
As miniaturization of sensors occurs, the platforms are proving more valuable
Line-of-sight (LOS) operations are the common pilot control method
Figure 4. Dragonflyer X6 VTOL UAS Image courtesy Dragonfly Innovations, Inc.
Figure 5. Aeryon Scout VTOL UAS. Image courtesy Aeryon Labs, Inc.

## Slide 11: Vertical Take-Off & Landing (VTOL)
An example of a mid-sized, commercially used VTOL UAS.
Employed primarily for agricultural spraying operations.
Payload capacity and endurance to support remote sensing system operations, and has flown with various experimental remote sensing systems at NASA-Ames Research Center.
Figure 6. The Yamaha RMAX VTOL aircraft, shown with a pesticide/herbicide application sprayer payload used in precision agriculture. Image courtesy of Yamaha Motor Australia.

## Slide 12: Vertical Take-Off & Landing (VTOL)
More Than 770,000 UAVs Now Registered In US, FAA Says.
Need for air traffic controlling system
Figure 3. Unmanned VTOL commercial platform systems developed (horizontal axis) by year between 1960-2012. Data for 2012 are estimates at the time of writing.
Notes: 3e

## Slide 13: Low Altitude, Short Endurance (LASE) and Low Altitude, Long Endurance (LALE)
Occur in an array of sizes and configurations, from back-packable, hand-launched platforms to catapult-launch platforms.
Operational capabilities of 45 min–2 h, and a reduced payload capacity.
Figure 7. LASE and LALE UAS on display at 2005 Naval Unmanned Aerial Vehicle Air Demo. Pictures are (front to back, left to right) RQ-11A Raven, Evolution, Dragon Eye, NASA FLIC, Arcturus T-15, Skylark, Tern, RQ-2B Pioneer, and Neptune. Image courtesy US Department of Defense.

## Slide 14: Medium Altitude, Long Endurance (MALE)
The SIERRA has supported several airborne science data collection campaigns, including the following missions:
  1. CASIE (2009): The Characterization of Arctic Sea Ice Experiment operated from Svalbard, Norway, above the Arctic Circle.
  2. RAM-GGM (2011): The Right-of Way Automated Monitoring-Greenhouse Gas Mission pilot study occurred in Railroad Valley, NV, USA.
  3. Long-Term Earthquake Hazards and groundwater measurement UAS (SIERRA) campaign (2011–2013).
  4. High Resolution Assessment of Carbon Dynamics in Seagrass and Coral Reef Biomes (2011–2013).
Figure 9. The NASA SIERRA, shown flying near Svalbard, Norway, 2009. Image courtesy NASA.

## Slide 15: Medium Altitude, Long Endurance (MALE)
20 m wingspan can loft payloads of nearly 200 kg internally, as well as external loads of 900 kg.
Capable of reaching altitudes above 12,000 m, but with limited endurance at that altitude.
Performance characteristics are optimized at 5,500 m to 9,000 m feet altitude, where the aircraft is capable of ~24-hour mission endurance.
Remote sensing data collection during its first campaign flights from 2007–2009
Figure 8. NASA Ikhana. Image courtesy NASA.

## Slide 16: Medium Altitude, Long Endurance (MALE)
Western States UAS Fire Imaging Missions, the aircraft flew over 20 missions in the western United States over 60 fires.
Over a period of three fire seasons, showcased the utility of UAS to support both scientific data collection and disaster monitoring capabilities.
Table 1 lists wildfire imaging support missions flown by Ikhana during the 2006–2009 fire seasons.

## Slide 17: High Altitude, Long Endurance (HALE)
More recent introduction into the UAS world.
Outside of the US Department of Defense, the major civilian components that have employed HALE UAS to support science have been NASA and NOAA.
Collect information at regional and global scales to support satellite observations at spatial and temporal scales.
Expensive
Figure 10. The Pathfinder HALE UAS. Image Courtesy NASA

## Slide 18: High Altitude, Long Endurance (HALE)
The Global Hawk has an operating altitude of 19,800 m and a flight endurance of over 30 h.
Cruises at 550 km/h and carries a payload of 750 kg for a range of over 17,000 km.
The platform has compartments that can house over 10 different instruments, supporting multiple science instrumentation measurement capabilities.
Future: Hurricane and Severe Storm Sentinel (HS3) will be a five-year mission specifically targeted to investigate the processes that underlie hurricane formation and intensity.
Figure 11. The NASA/NOAA Global HAWK HALE UAS. Image courtesy NASA.

## Slide 19: Regulations
June 21, 2016
Part 107 of the Federal Aviation Regulations

## Slide 20: Main Paper
    Using the MicroASAR on the NASA SIERRA UAS in the Characterization of Arctic Sea Ice Experiment
    Evan Zaugg, David Long, Matthew Edwards, Matthew Fladeland, Richard Kolyer, Ian Crocker, James Maslanik, Ute Herzfeld, and Bruce Wallin
    May 2010

## Slide 21: CASIE
CASIE-09 (Characterization of Arctic Sea Ice Experiment 2009)
NASA Mission to study sea ice roughness and break-up in the Arctic and high northern latitudes.
Photos courtesy of CASIE Blog

## Slide 22: CASIE Objectives
Determine the degree to which ice-roughness monitoring via remote sensing can detect basic changes in ice conditions such as ice thickness and ice age.
Investigate relationships between ice roughness and factors affecting the loss or maintenance of the perennial ice cover.
Determine how roughness varies as a function of different kinematic conditions and ice properties.
The mission offers a technological and operational testbed to demonstrate the value of autonomous vehicles for long-range, long-duration remote sensing science.

## Slide 23: SIERRA
Sensor Integrated Environmental Remote Research Aircraft
The NASA SIERRA UAS and the CASIE team in Ny-Alesund, Svalbard, Norway.
NASA SIERRA UAS 3-View and Specifications

## Slide 24: Sea Ice
Drives ocean currents around the world
Winds and currents move ice sheets and cause them to raft.
The melting of sea ice drives ecosystems and affects global climate.
https://youtu.be3/u12QJVmr3YU

## Slide 25: Arctic Sea Ice Animation 2000-2016
NASA's Scientific Visualization Studio (https://svs.gsfc.nasa.gov/4510)

## Slide 26: September 1984 vs 2016
NASA's Scientific Visualization Studio (https://svs.gsfc.nasa.gov/4510)

## Slide 27: What is ASAR?
Airborne Synthetic Aperture Radar
https://www.youtube.com/watch?v=0SIhWWgzE1w

## Slide 28: How does SAR work?
Can see through the dark and through clouds.
To make images using echo location, two things are needed:
1. Where each echo came from on the ground.
2. How bright each echo should be in the image.

## Slide 29: 1. Where each echo came from on the ground
A. Frequency modulated continuous-wave (FMCW) and time give us the distance.
B. Doppler Effect tells us where along the distance.

## Slide 30: 2. Determining brightness of each echo
I= Ioexp(-4πniz/λ)
r

## Slide 31: Index of Refraction in Microwave
Water
  Real ~ 8 (Reflection)
  Imaginary ~ 1 (absorption)
Ice
  Real ~ 2 (Reflection)
  Imaginary ~ 0.4 x10-4 (absorption)
Similarly, a conventional microwave oven operates at wavelength of ~12 cm.
~ 55 mm

## Slide 32: SAR Imaging
A series of images collected during the CASIE mission showing agreement between the MicroASAR sensor (top) and the on board video camera (bottom).

## Slide 33: SAR Imaging
Greyscale backscatter intensity.
Color-enhancement of (a) to visually improve
differentiation of surface reflectance properties.
(c)-(f) are vario-parameters derived by application of geostatistical classification algorithms.
(c) pond parameter (overall roughness),
(d) mindist parameter (average size/ spacing of significant spatial features).
(e) parameter p1 absolute significance of spatial features (as found by mindist).
(f) parameter p2 (relative significance of spatial features, as found by mindist)

## Slide 34: Concluding Remarks
Successes:
  Fine spatial resolution
  Difficult to access locations in high arctic
  UAS is preferred platform over satellites, piloted aircrafts, and ground measurements.
Challenges:
  Changes in ice topography and roughness affect dynamic and thermodynamic properties.
  Quantifying the degree to which these changes affect ice growth feedback loops.
  Identification of sea ice types
  Accounting for open water vs thin ice coverage
  Ground observation validation

## Slide 35: References
Chirica, Dan. "CASIE." NASA. NASA, 5 Dec. 2013. Web. <https://espo.nasa.gov/home/casie>.
Starr, Cindy. "Weekly Animation of Arctic Sea Ice Age with Graph of Ice Age By Area: 1984 - 2016." NASA. NASA, 28 Oct. 2016. Web. 23 Apr. 2017. <https://svs.gsfc.nasa.gov/4510>.
Watts, A.C.; Ambrosia, V.G.; Hinkley, E.A. Unmanned Aircraft Systems in Remote Sensing and Scientific Research: Classification and Considerations of Use. Remote Sens. 2012, 4, 1671-1692.
Zaugg, Evan, David Long, Matthew Edwards, Matthew Fladeland, Richard Kolyer, Ian Crocker, James Maslanik, Ute Herzfeld, and Bruce Wallin. "Using the MicroASAR on the NASA SIERRA UAS in the Characterization of Arctic Sea Ice Experiment." IEE Explore. 2010 IEEE Radar Conference, May 2010. Web.

## Slide 36: Questions/Discussion