## Slide 1: Water Resources and Changing Climate
A Presentation by Will Boyer
For ATMS 790

## Slide 2: April 6th -7th Storm
Yosemite Valley, CA

## Slide 3: April 6th -7th Storm
Yosemite at Happy Isles (data since 1916)
5 historic days with more total volume (3 storms)
4th largest storm by single day flow
~25 Yr. recurrence interval
All similar storm related flooding has occurred Nov.– Feb. !!!!

## Slide 4: April 6th -7th Storm
North Fork American River (data since 1941)
75 historic days with more total volume
3 Days in April or later with more total volume (2 storms)
Majority of historic storm related flooding prior to April!!!!

## Slide 5: Merced River
24 hr. period
04/06– 04/07
9AM to 9AM
Received around 4 inches of precipitation

## Slide 6: North Fork American River
24 hr. period
04/06– 04/07
9AM to 9AM
Received around 4 inches of precipitation

## Slide 7: Reason for difference?
---Short, intense precipitation event
Lots of exposed granite bedrock in Yosemite, making Merced River extremely “flashy” drainage.
(highly susceptible to quick runoff response)

## Slide 8: Impacts to Truckee River and Tahoe
”Emergency” Releases from Tahoe begin on 04/02 in preparation
Tahoe still rises ~3” from storm
Truckee River sees highest storm related (not snowmelt) daily flow volume, ever for April or later
Tahoe Level
Truckee River Below Tahoe
Truckee River at Farad (~35 miles downstream)

## Slide 9: Where does that leave us for snowpack and total annual precip?

## Slide 10: Where does that leave us currently for snowpack and total annual precip?
Snowpack Stats As of Today (04/09/2018) |  |  | 
Snotel Site Name | Elevation (Ft) | SWE % of Average | Precip % of Average
Mt Rose Ski Area | 8801 | 91 | 94
Squaw Valley G.C. | 8013 | 64 | 87
Echo Peak | 7653 | 60 | 97
Donner Summit | 6894 | 51 | 97
Independence Creek | 6436 | 48 | 85

## Slide 11: Why snowpack is important
Western US has very seasonal precip, needs dry season (summer) water reserves
Snowmelt gives more predictable and controlled reservoir fill than storms
Snowpack acts as natural reservoir, releasing water into summer
Example for Truckee River, NV

## Slide 12: Why snowpack is important
In California:
~70% of SoCal water supply is from imported sources
  75% of which comes from spring snowmelt
Majority of Central Valley water supply comes from spring snowmelt
  Large warm winter storms and flood waters often discharged to Sacramento Delta, without efficient storage mechanism
Mid-century snowpack projected to decrease by 33%-70% in Sierra Nevadas
Snowpack decrease of 20%-29% projected for Rockies

## Slide 13: Climate and Hydrology Modeling (via Brianna R Pagan et al., 2016)
Variable Infiltration Capacity (VIC) hydrology model
3 hr time step
5 elevation bands for topography and Precip.
10 AOGCMs at 18km grid spacing form an ensemble
AOGCMs downscaled to 4 km horizontal grid spacing
INPUTS:
Daily min and max T
Daily Precip.
10m winds
RCP 8.5 used for AOGCMs
OUTPUTS:
Precip (P)
Runoff (Q)
SWE
Snow depth
Soil Moisture
Temp (T)
Albedo

## Slide 14: Relative Concentration Pathways
This Study Uses

## Slide 15: Climate and Hydrology Analyses (via Brianna R Pagan et al., 2016)
Model OUTPUTS:
Precip (P)
Runoff (Q)
SWE
Snow depth
Soil Moisture
Temp (T)
Albedo
Compared between
Baseline Period
1976-2005 Hydrology
Future RCP 8.5
years 2021-2050
Additionally
Generalized extreme value (GEV) distribution
  Fit to both Max. and annual one-day P and Q events
  Evaluates future changes in return period of extreme events

## Slide 16: Water Balance Equation
  Q = runoff
  P = precipitation
  ET = evapotranspiration
  = change in storage
  (often assumed = 0 over time)

## Slide 17: Climate and Hydrology Implications
Temp increase up to 2℃
Greater increases in mountains, due to snow-albedo feedback
Decreased snowpack January – April due to warmer temps and decreased snow to P ratio
Albedo decreases most during winter, due to less snowpack

## Slide 18: Climate and Hydrology Implications
Generally slight increase in overall P
P becomes more seasonal, with increases in Winter and decreases in Spring
Increase in overall ET, due to warmer temps
  Water Balance:
Change in Q is mixed, due to competing effects of P and ET, but generally Q decreases in Mtns.
Runoff shifts 6-11 days earlier

## Slide 19: Precip. Frequency Implications (Daily)
Probability of Occurrence (?)
One Day Max P 50 yr. event becomes 8-28 yr. event
50 yr. Q event becomes 6 - 1.6 times more likely
Precip. and Runoff volumes increase similarly

## Slide 20: Precip. Frequency Implications (annual)
Probability of Occurrence (?)
General increase in volume of annual max runoff
General decrease in annual min runoff, with greater drying in mountainous regions
Possibility for greater annual variability including an increase in both wet and dry years.

## Slide 21: Characteristics of regions with water supplies most susceptible to climate change impacts:
Snowmelt dominated Runoff
Highly Seasonal Precipitation Patterns
Lower elevation watersheds with mountain tops closer to snowline
Unpredictable weather events, or a range of possible storm patterns

## Slide 22: Characteristics of regions with infrastructure limitations and anthropogenic stresses:
Little reservoir storage or no available water storage facilities (like the Carson River)
Inflexible timing of reservoir operations
Large or rapidly growing populations

## Slide 23: Case Study: Dam ops on the Truckee River
Truckee River system entirely dam controlled
Climate Change impacts indicate a 2-3 week shift in snowmelt runoff by 2050
Dam flood safety requirements specify that reservoir filling can’t begin until April

## Slide 24: Case Study: Dam ops on the Truckee River
Allowing the reservoirs to begin filling 2 months earlier, substantially increases available water supplies during droughts!
*Drought supply modeling performed for TMWA water supply system, using a 15-yr. drought scenario calibrated to 2050 climate conditions

## Slide 25: Caveats…this March and last storm
Very unusual, with the last runoff event being the largest of its type (storm flood and not snowmelt) this late in the year.
Majority of local high flow events in Nov. – Feb timeframe.

## Slide 26: Solutions: Bigger Dams?
Pros
  More storage Space to Capture and store flood water
Cons
  Increasing evaporation losses with climate change
  Serious regional environmental impacts
  Methane emissions contribute to greenhouse gas increases (est. as much as 4% of total warming impact of human activities)
Matilija Dam near Ventura

## Slide 27: Solutions: MAR (Managed Aquifer Recharge)

## Slide 28: MAR (Managed Aquifer Recharge)
Pros
  Helps restore declining aquifer levels and health
  No evaporation losses
  Could potentially store large volumes of flood water
Cons
  Potentially expensive and often energy intensive
  Can pick up agricultural chemicals or nutrients and bring to groundwater (Ag Mar specific)
  Difficult accounting -anyone with a nearby well could potentially be “stealing” your recharged water

## Slide 29: Solutions: FIRO (Forecast Informed Reservoir Operations)
Ongoing study performed for Lake Mendocino, on the Russian River, by the Center for Western Weather and Water Extremes

## Slide 30: FIRO (Forecast Informed Reservoir Operations)
Pros
  Simply a change in operating regime, no new infrastructure is required
  Increases efficiency of reservoir storage operations
  Increases amount of available drought reserves
Cons
  Requires fairly consistent and predictable weather
  Requires reliable 5-9 weather forecast
  Potentially dangerous operations if forecast is inaccurate

## Slide 31: Is climate change currently being seen in western US hydrology?
Extreme variability has been occurring recently!
2012-2015 drought worst 4 years on record
Followed shortly by 2017 as the wettest single year ever recorded
WY 2018 very dry beginning, followed by exceedingly wet March and April

## Slide 32: Is climate change currently being seen in western US hydrology?
YR | DOY
1940 | 236.27
2020 | 228.95
Historical runoff data shows an observed shift of about 2 weeks in timing since 1940
Merced River in Yosemite

## Slide 33: Is climate change currently being seen in western US hydrology?
Merced River in Yosemite

## Slide 34: Is climate change currently being seen in western US hydrology?
Historical runoff data shows an observed shift of about 2 weeks in timing since 1940
North Fork American River
YR | DOY
1940 | 178.274
2020 | 164.362

## Slide 35: Questions?